## Slide 1: Numerical Integration
himanshu@iitmandi.ac.in
Dr. Himanshu Pathak

## Slide 2: Numerical Integration
Evaluate the integral, without doing the calculation analytically.
In essence, Integrand is too complicated to integrate analytically.
sum of height  width
f(x)
x
where
Integration is a summing process. Thus virtually all numerical approximations can be represented by
wi are the weights, xi are the sampling points, and Et is the truncation error.

## Slide 3: Newton-Cotes Integration
1st order Polynomial
By Newton-Cotes formulas
Newton-Cotes formulas are the most common numerical integration schemes.
It replaces a complicated function with an approximating function that is easy to integrate numerically.
2nd order Polynomial
1st order Polynomial segment wise

## Slide 4: Trapezoidal Rule
The trapezoidal rule is the first order example of the Newton-Cotes closed integration formulas.
Trapezoidal Rule
Using linear interpolation

## Slide 5: Trapezoidal Rule
Trapezoidal Rule

## Slide 6: Trapezoidal Rule
Trapezoidal Rule
Example: Numerically integrate the following polynomial
f(x)= 0.2 + 25x - 200x2 + 675x3 - 900x4 + 400x5 from a = 0 to b = 0.8.
The exact value of the integral can be determined analytically to be 1.640533.
Integral
Turncation Error

## Slide 7: Multiple-Application Trapezoidal Rule
One way to improve the accuracy of the trapezoidal rule is to divide the integration interval from a to b into a number of segments and apply the method to each segment.
The areas of individual segments can then be added to yield the integral for the entire interval.
The resulting equations are called multiple-application, or composite, integration formulas.
n + 1 equally spaced base points (x0, x1, x2, . . . , xn).
n segments of equal width
Segment Width
Total Integrals

## Slide 8: Multiple-Application Trapezoidal Rule
Multiple-Application Trapezoidal Rule
Example: Numerically integrate the following polynomial
f(x)= 0.2 + 25x - 200x2 + 675x3 - 900x4 + 400x5 from a = 0 to b = 0.8.
The exact value of the integral can be determined analytically to be 1.640533.
Integral
Turncation Error
2 segments
5 segments

## Slide 9
MATLAB© Script
MATLAB Program for Multiple-Application Trapezoidal Rule
clear all
clc
a= 0; % lower limit
b = 0.8; % upper limit
c = 10; % No of segments
x=linspace(a,b,c+1); % point generation
n=length(x);
h = (b-a)/(n-1);
sum= 0;
for i=2:n
X1 = int_fun(x(i-1));
X2 = int_fun(x(i));
sum = sum + h*((X1 + X2)/2);
end
sum

## Slide 10: Simpson’s Rule
One way to improve the accuracy of the trapezoidal rule is to use higher order polynomial in function approximation.
As compared with Trapezoidal rule (function is approximated by first order polynomial); Simpson’s 1/3 rule use second-order Lagrange polynomial for each integrant segment.
Simpson’s 3/8 rule use third-order Lagrange polynomial for each integrant segment.
2nd order (Simpson’s 1/3)
3rd order (Simpson’s 3/8)

## Slide 11: Simpson’s 1/3 Rule
A second-order interpolating polynomial is substituted the integrant.
Simpson’s 1/3 Rule
If a and b are designated as x0 and x2 and f2(x) is represented by a second-order Lagrange polynomial.

## Slide 12: Simpson’s 1/3 Rule
Simpson’s 1/3 Rule
Example: Numerically integrate the following polynomial
f(x)= 0.2 + 25x - 200x2 + 675x3 - 900x4 + 400x5 from a = 0 to b = 0.8.
The exact value of the integral can be determined analytically to be 1.640533.
Integral
Truncation Error
Approximately 5 times more accurate than for a single application of the Trapezoidal rule

## Slide 13: Multiple-Application Simpson’s 1/3 Rule
One way to improve the accuracy of the Simpson’s 1/3 Rule is to divide the integration interval from a to b into a number of segments and apply the method to each segment.
The areas of individual segments can then be added to yield the integral for the entire interval.
n + 1 equally spaced base points (x0, x1, x2, . . . , xn).
n segments of equal width
Segment Width
Total Integrals

## Slide 14: Multiple-Application Simpson’s 1/3 Rule
Multiple-Application Simpson’s 1/3 Rule
Example: Numerically integrate the following polynomial
f(x)= 0.2 + 25x - 200x2 + 675x3 - 900x4 + 400x5 from a = 0 to b = 0.8.
The exact value of the integral can be determined analytically to be 1.640533.
Integral
Truncation Error

## Slide 15: Simpson’s 3/8 Rule
A third order Lagrange polynomial can be fit to four points and integrated.
Simpson’s 3/8 Rule
Here, f3(x) is represented by a third-order Lagrange polynomial.

## Slide 16: Simpson’s 3/8 Rule
(a) Simpson’s 3/8 Rule
Example: Numerically integrate the following polynomial
f(x)= 0.2 + 25x - 200x2 + 675x3 - 900x4 + 400x5 from a = 0 to b = 0.8.
(a) Use Simpson’s 3/8 rule (b) Use Simpson’s 1/3 and Simpson’s 3/8 for total 5 segments
Integral
Truncation Error
Requires four equally spaced points

## Slide 17: Simpson’s 3/8 Rule
(b) Simpson’s 1/3 and Simpson’s 3/8
Example: Numerically integrate the following polynomial
f(x)= 0.2 + 25x - 200x2 + 675x3 - 900x4 + 400x5 from a = 0 to b = 0.8.
(a) Use Simpson’s 3/8 rule (b) Use Simpson’s 1/3 and Simpson’s 3/8 for total 5 segments
Integral for the first two segments is obtained using Simpson’s 1/3 rule
Truncation Error
Requires atleast 6 equally spaced points or 5 segments
Integral for the last three segments is obtained using Simpson’s 3/8 rule
Total Integral

## Slide 18
MATLAB© Script
MATLAB Program for Simpson’s 1/3 Rule
clear all
clc
a= 0; % lower limit
b = 0.8; % upper limit
x=linspace(a,b,3);
y = int_fun(x);
Integral = (b-a)*(y(1) + 4*y(2) + y(3))/6
clear all
clc
a= 0; % lower limit
b = 0.8; % upper limit
c = 2; % No of segments
x=linspace(a,b,2*c+1); % point generation
n=length(x);
h = (b-a)/(n-1);
for i=1:n
y(i) = int_fun(x(i));
end
Segment=sum(y(:,1:2:end-2)+4*y(:,2:2:end-1)+y(:,3:2:end),1)*h/3;
Integral = sum(Segment)

## Slide 19
MATLAB© Script
MATLAB Program for Simpson’s 3/8 Rule
clear all
clc
a= 0; % lower limit
b = 0.8; % upper limit
x=linspace(a,b,4);
y = int_fun(x);
Integral = (b-a)*(y(1) + 3*y(2) + 3*y(3) + y(4))/8
function y = int_fun(x)
% Function for integration purpose
y = 0.2 + 25*x - 200*x.^2 + 675*x.^3 - 900*x.^4 + 400*x.^5;

## Slide 20: Integration with Unequal Segments
Integration scheme, if segement size is not equal.
Apply trapezoidal rule to each segment and sum the results:
Segment wise Trapezoidal Rule
Segment data:

## Slide 21: Newton-Cotes Integration

## Slide 22: Gauss Quadrature
Weighted sum of function values at specified points within the domain of integration.
Gauss Quadrature Approximation (two points)
Gauss Quadrature Approximation (higher points)
Limit Conversion

## Slide 23: Gauss Quadrature
Conversion of integration limit
Example: Numerically integrate the following function:
Three point Gauss Quadrature

## Slide 24: Gauss Quadrature

## Slide 25: Gauss Quadrature
Gauss Point (n) | Integration Value (I) | Relative Error (ε)
1 | 1.036 | 15.89
2 | 0.9101 | 1.89
3 | 0.8942 | 0.03
4 | 0.8939 | 0

## Slide 26
Questions??
THANK YOU